## Slide 1: Introduction to image analysis
With Fiji (ImageJ and others)
Daniel Waiger, HUJI, FACSI
FACSI - Faculty of Agriculture Center for Scientific Imaging
With material from
Robert Haase, Physics of Life, TU Dresden

## Slide 2
Major credit * 106 to…
https://git.mpi-cbg.de/rhaase/lecture_applied_bioimage_analysis_2020
Robert Haase, Physics of Life, TU Dresden
For sharing his slides and for his important contribution to the field of image analysis
Lecture BioImage Analysis 2020

## Slide 3
This is
image beautification,
not image analysis
Camera image source: André Karwath aka Aka, CC BY-SA 2.5, https://creativecommons.org/licenses/by-sa/2.5
https://en.wikipedia.org/wiki/Camera#/media/File:Nikon_D200_front_(aka).jpg

## Slide 4
-
=
Image analysts use similar tools e.g. for feature extraction, and you are going to learn how they work.

## Slide 5
5
Open-Source software
Proprietary/Commercial/Licensed software
And there are many others

## Slide 6
Image sources: Akanksha Jain, Tomancak lab, MPI CBG (SPIM image)
https://commons.wikimedia.org/wiki/User:Acagastya (Miroscope, public domain)
Muhammad Mahdi Karim (Drosophila, GFDL 1.2)
Image processing
Imaging
Volume in ml
Ant based delineation
Delineation from exp. observers
Box plot (Volume)
Image analysis
Bio-statistics
Modeling
Observation
IMAGE ANALYSIS IS A PART OF THE EXPERIMENT !

## Slide 7
Bio-image analysis is supposed to be quantitative
The left image contains less mandarines than the image on the right.
The right image contains several mandarines.
Mandarine count
Left: 0
Right: 3

## Slide 8
Bio-image analysis is supposed to be reliable

## Slide 9
Bio-image analysis is supposed to be objective
Observer 1:
17.3 ml
Observer 2:
7.5 ml
Observer 3:
9.9 ml
Automatic segmentation:
8.2 ml
Three experts outlining a tumor on Positron Emission Tomography data
One computer executing the same task
Data source: N. Abolmaali, R. Haase, Oncoray, TU Dresden

## Slide 10
https://forum.image.sc/t/quantifying-fluorescence-intensity-of-confocal-microscope-images/99960/2?u=daniel_waiger

## Slide 11
Bio-image analysis is supposed to be reproducible
  Experiments must be documented so that others can repeat them.

## Slide 12
Bio-image analysis is supposed to be repeatable
  The experiment must be designed so that one can repeat it with the same sample.

## Slide 13
https://www.youtube.com/watch?v=e-2DbkUwKk4&list=PL5ESQNfM5lc7SAMstEu082ivW4BDMvd0U&index=1
Notes: Start at: 12:08 End: 14:26

## Slide 14
Bio-image analysis is supposed to be
  Quantitative
    We derive numbers from images which describe physical properties of the observed sample.
  Objective
    The derived measurement does not depend on who did the measurement. The measurement is free of interpretation.
  Reliable
    We are confident that the measurement is describing what it is supposed to describe.
  Reproducible
    Somebody else can do the experiment under different conditions and gets similar measurements. For this, documentation is decisive!
  Repeatable
    We can do the same experiment twice under the same conditions and get a similar measurements.

## Slide 15: Images and pixels
An image is just a matrix of numbers
Pixel: “picture element”
The edges between pixels are an artefact. In reality, they don’t exist!
0
255

## Slide 16
Images and pixels
Quantifying fluorescence is not as trivial as you think!

## Slide 17
Pixel size versus resolution
Pixel size is a digital property of an image.
You configure it during the imaging session at the microscope.
Pixel size: 3.3 µm
Pixel size: 0.8 µm
Pixel size: 0.05 µm
We are not talking about resolution!
The “canvas” area is the same in all three cases.

## Slide 18
Pixel size versus resolution
Pixel size is a digital property of an image.
You configure it during the imaging session at the microscope.

## Slide 19
https://www.youtube.com/watch?v=jp2Q2g0A5wc
Notice the increase in px size
Pixel size versus resolution

## Slide 20
Pixel size versus resolution
Resolution is a property of your imaging system.
The measure of how close objects can be in an image while still being differentiable, is called spatial resolution – and it depends on our question!

## Slide 21: Bit-depth
A bit is the smallest memory unit in computers.
The bit-depth n enumerates how many different intensity values are present in an image:
  2n grey values
In microscopy, images are usually stored as 8, 12 or 16-bit images.
1
2
3
4
5
6
7
8
1
2
16

## Slide 22
Bit-depth: Pitfalls
When working with 8-bit images, 256 different gray values can be saved.
That’s usually the numbers 0-255.
Depending on software:
  100 – 200 = 0
  100 – 200 = 155
  100 + 200 = 255
  100 + 200 = 45
Solution: When doing math with pixels, avoid bit-depth 8!

## Slide 23
Lookup tables
The lookup table decides how the image is displayed on screen.
Applying a different lookup table doesn’t change the image. All pixel values stay the same, they just appear differently
Pixel value
Display color
0
1
2
…
255
Pixel value
Display color
0
1
2
…
255
Pixel value
Display color
0
1
2
…
255

## Slide 24
Lookup tables
Choose visualization of your color tables wisely!
Think of people with red/green blindness!
Default view
Red/green blind people see it like this
Replace red with magenta!
Any of you doesn't see the difference?

## Slide 25: Lookup tables
Lookup tables are a free choice.
They may (or may not) express which wavelengths has been imaged before.
Hint: Try not to do arts.

## Slide 26
Remember them?

## Slide 27
Trackmate
Core ImageJ
Fiji is just ImageJ – Included with ninja skills.
Ridge detection
TrakEM
StarDist
FigureJ
The list is long, but there is a tool for everyone!

## Slide 28
Included plugins for many purposes
  Flexibility 
  Applicability 
  User experience 
  Maintenance 
Optional plugins: http://imagej.net/List_of_update_sites
  Extensibility 
https://twitter.com/haesleinhuepf/status/1288372583495327744
Fiji – a true story of love and hate

## Slide 29: Fiji user experience
The menus are confusing and not very well organized
Use the search field!
  It shows you where the plugin is located
  You can run it from here (press enter)
  Allows you searching
    for plugins / menus
    Operations (ops)
    ImageJ wiki
    Forum

## Slide 30
Fiji example workflow
Popular basic analysis fluorescence pipeline: thresholding + particle analysis
From images to raw data for statistics and *omics post-processing
Always Duplicate your image(s) – *Never apply threshold!

## Slide 31: Fijis user interface
There are more tools hidden in the toolbar than expected…
Use the right click to discover them!

## Slide 32: Distance measurements
For simple distance measurements, use the line tool and observe the status bar of FIJI

## Slide 33: Distance measurements
Use the M key to store a length-measurement to the results table.

## Slide 34
Current color channel
Current slice-position in space
Current position in time (frame number)
Zoom factor
Image type
Image size in physical units (and in pixels)
Fijis user interface

## Slide 35: Correct pixel size
Set pixel size by using Image > Properties
Analyze > Set scale is a workaround; it’s not precise!
Here you can enter “um” instead of “µm”. It will be interpreted as micrometer

## Slide 36
Fiji basics – Measurement tools.
https://youtu.be/Akedfyp5AxY
Notes: Start: 06:50 End: 10:50

## Slide 37: Visualisation: brightness / contrast
After opening an image, adjust Brightness & Contrast in order to *see* it properly
Use the menu Image > Adjust > Brightness & Contrast (CTRL+SHIFT+C)

## Slide 38: Visualisation: brightness / contrast
After opening an image, adjust Brightness & Contrast in order to *see* it properly
Use the menu Image > Adjust > Brightness & Contrast (CTRL+SHIFT+C)

## Slide 39: Visualisation: brightness / contrast
After opening an image, adjust Brightness & Contrast in order to *see* it properly
Use the menu Image > Adjust > Brightness & Contrast (CTRL+SHIFT+C)

## Slide 40: Visualisation: brightness / contrast
Define the grey value range to visualize
Also known as “windowing”
Menu Image > Adjust > Brightess/Contrast or Ctrl+Shift+C
Try to “window” the object you would like to see best.
This may be the “hill” in the histogram

## Slide 41: Channel selection
In multi-channel images, brightness and contrast must be configured for channels individually

## Slide 42: Channel selection
Intensity measurements depend on the selected channel!

## Slide 43: Lookup tables
Choose visualization of your color tables wisely!
Think of people with red/green blindness!

## Slide 44: Regions of interest (ROI)
draw a rectangle
using the rectangle tool
draw a circle
using the circle tool
add objects to the ROI
by holding SHIFT
unite objects to the ROI
by holding SHIFT
subtract objects to the
ROI by holding ALT
move the ROI
by clicking inside and move the mouse
delete the ROI
by clicking outside
Recover the last ROI by using menu Edit > Selection > Restore Selection (SHIFT+CTRL+E)

## Slide 45
Fiji basics – Exercise 1.
Take 10 min. to find out how many blobs are in the image.

## Slide 46
Blobs  Threshold  Set Measurements  Analyze Particles  !Results!
Fiji example workflow
Popular basic analysis pipeline: thresholding + particle analysis
From images to raw data for statistics and *omics post-processing

## Slide 47: Fiji example workflow
From a multichannel z-stack (3D) to 3 separate 2D images.
Notice the Channel and Z sliders

## Slide 48: Fiji example workflow
Channel 1 = DAPI (BLUE)
Channel 3 = FIBRILLARIN (RED)
Channel 2 = BRIGHTFIELD
Step 01: Channel splitting
Image > Color > Split Channels
Notice the Z slider

## Slide 49: Fiji example workflow
Channel 1 = DAPI (BLUE)
Channel 3 = FIBRILLARIN (RED)
Brightfield image is not useful in this case
Step 02: Applying LUTs – For ease of viewing our organelles (Cyan Hot – Blue) / (Red Hot – Red)
Image > Lookup Tables > LUT of choice
Notice that we haven’t manipulated our data, we just view it in with arbitrary color(s).
OPTIONAL

## Slide 50: Fiji example workflow
Steps 03-04: Counting particles
Analyze > Set Measurements> Tick boxes.
Analyze > Analyze Particles> Choose Min-Max particle size (in um^2 or pixel^2)> Tick boxes.

## Slide 51: Fiji example workflow
Step 05: Merging Channels– For recombining our images into one new image (Cyan Hot – Blue) / (Red Hot – Red)
Image > Color> Merge Channels (remember which channel was which color).
OPTIONAL

## Slide 52
Few messages from our sponsors:
In imaging (including image analysis), S**T IN = S**T OUT!
Seeing is believing
Measuring is science!
Also:

## Slide 53
Image integrity and standards
Figure and Video Guidelines | Journal of Cell Biology | Rockefeller University Press (rupress.org)

## Slide 54
Image integrity and standards
Image integrity and standards | Nature Portfolio

## Slide 55
Image integrity and standards
Instructions for preparing an initial manuscript | Science | AAAS (sciencemag.org)

## Slide 56
Macro programming - resources
Each image is a clickable link
At least try exercise #1 – that’s the best and easiest way to start
Take your time here, Anna is a great teacher!
Good for weekends.

## Slide 57
(46) Johanna M. Dela Cruz - YouTube
(46) haesleinhuepf - YouTube
NEUBIAS - YouTube
Softwre Tutorials - resources

## Slide 58
Microscopy for Dummies (zeiss.com)

## Slide 59
Questions?
Keep in mind: It is an intro; we’re not expecting you to remember it all today.

## Slide 60
Fiji & reproducible research: macros (Automation)
The macro recorder and the script editor allow scripting Fiji and thus, reproducible workflows.
Run workflows on hundreds or thousands of images!
Runs on the background

## Slide 61
Macro recorder
Choose IJ1 Macro as the language for your script

## Slide 62
Bio-image analysis is supposed to be reliable

## Slide 63
https://github.com/image-analysis/micro-formats-extractor
Micro-Formats Extractor

## Slide 64
Plugins: FigureJ – image panel creation
Schematic overview of an example workflow – from 2D nuclei to particle count within them (on a different channel).

## Slide 65
Basic generalizing your macro

## Slide 66
Plugins – Stardist, ilastik, clij2, how to install

## Slide 67
Metadata is important
What microscope was he using?
Or in other words – this guy knows that in microscopy it’s shit in = shit out!

## Slide 68
PLUGINS SHOWCASE

## Slide 69
Plugins: StarDist 2D – Automatic nuclei segmentation - DAPI

## Slide 70
Plugins: WEKA – same as ilastik (but only as pixel classification workflow)

## Slide 71
Plugins: StarDist 2D – Automatic nuclei segmentation – H&E staining
Not perfect – can be adjusted for better results!

## Slide 72
Software: Ilastik (also a Fiji plugin)

## Slide 73
Software: Ilastik (also a Fiji plugin)

## Slide 74
NEED HELP?

## Slide 75
Let’s work on the practical – FIJI TRAINING

## Slide 76
imaris
Raw confocal data
3D rendering w/imaris
Blue/Red Dots – Oly protein
Green – α-Tubulin filaments
Co-localization of mutant protein on α-Tubulin filaments

## Slide 77
One last thing about protocols…
How mounting media can affect tissue thickness:
https://twitter.com/patrina_pellett/status/824692850285645824

## Slide 78
1
2
Take it from the pros…(from previous slide)